## Slide 1
Simultaneous System Identification and Model
Predictive Control with No Dynamic Regret
Hongyu Zhou, Vasileios Tzoumas

## Slide 2
Robots That Learn Continuously Across Tasks & Domains
Lifelong/Continual Learning
Isolated/Self-supervised Learning
On-the-fly/Online Adaptation
Focus of this work
Increasing
Difficulty & Autonomy

## Slide 3
Robots That Adapts Continuously Across Tasks & Domains
Drone Delivery
Inspection & Maintenance
Target Tracking
Goal: Generate control inputs to achieve agile and accurate motion control across tasks & domains.1,2,3
Challenges: Dynamics and/or disturbances that are unknown, difficult-to-model, adaptive:
Drone delivery: Packages with unknown weights.
Inspection and maintenance: Wind, drag, ground effects.
Target tracking: Targets with unknown dynamics.
1 Ackerman, IEEE Spectrum '13
2 Chen, Liu, Shen, IROS '16
3 Seneviratne, Dammika, et al., Acta Imeko '18

## Slide 4
Model Predictive Control Under Uncertainty
All above scenarios are control problems under uncertainty
Goal: Find control input to minimize a look-ahead cumulative loss:
convex
known system dynamics
unknown uncertainty
control constraints

## Slide 5
Model Predictive Control Under Uncertainty
All above scenarios are control problems under uncertainty
Goal: Find control input to minimize a look-ahead cumulative loss:
Ideally: if is known:
convex
known system dynamics
unknown uncertainty
control constraints

## Slide 6
Model Predictive Control Under Uncertainty
All above scenarios are control problems under uncertainty
Goal: Find control input to minimize a look-ahead cumulative loss:
But is unknown:
convex
known system dynamics
unknown uncertainty
control constraints

## Slide 7
System Identification given a Function Basis
Goal: Find online
Example:
Neural Networks: Similarly to above but where:
Reproducing Kernels in Hilbert Spaces: Universal approximation theorem:4
[TRO '25]
Koopman Observables:
[ACC '25]
4 Boffi et al, JMLR '22

## Slide 8
System Identification given a Function Basis
Goal: Find online
Example:
Neural Networks: Similarly to above but where:
4 Boffi, et al, JMLR '22
Reproducing Kernels in Hilbert Spaces: Universal approximation theorem:4
[TRO '25]
Koopman Observables:
[ACC '25]

## Slide 9
Simultaneous System Identification and Model Predictive Control
i.e., update estimate of

## Slide 10
Suboptimality Metric against Optimal Control Policies in Hindsight

## Slide 11
State of the Art
5
6
5 Sánchez-Sánchez et al., '18; Carron et al., RAL '19; Torrente et al., RAL '21; Shi et al., ICRA '19; O’Connell, et al., SR '22; …
6 Goel et al., '20; Sabag et al., ACC '21; Goel et al., L4DC '21; Martin et al., L4DC '22; Didier et al., L-CSS '22; Zhou et al., CDC '23; …

## Slide 12
State of the Art
7
8
7 Slotine, '91; Krstic, et al., '95; Ioannou et al., '96; Tal et al., TCST '20; Wu, et al., '23; Das et al., '24; Jia, et al., TRO '23; …
8 Agarwal et al., ICML '19; Hazan et al., ALT '20; Gradu et al., L4DC '23; Zhou et al., CDC '23; Zhou et al., RAL '23; ...

## Slide 13
Algorithm: Simultaneous Sys-ID and MPC

## Slide 14
No Dynamic Regret
Theorem [TRO '25]

## Slide 15
Assumptions
Definition (Value Function9)
9 Grimm, et al, TAC '05

## Slide 16
Assumptions
Assumption (Stability Condition)
9 Grimm, et al, TAC '05
Assumption (Lipschitzness)

## Slide 17
Simulations on Cart-Pole Stabilization with Inaccurate Model
Goal:
Stabilize the cart-pole around the upright position of the pole
Setup:
The model parameters (pole length & mass, cart mass) are inaccurate
Compared algorithms: (i) Non-stochastic MPC10 and (ii) Gaussian Process MPC11
10 Zhou et al., RAL '23
11 Hewing et al., TCST '19
Ours
NS-MPC
GP-MPC

## Slide 18
Our Algorithm Achieves Fastest Stabilization
Results:
Our method achieves fastest stabilization while other algorithms:
  NS-MPC has marginal improvement over Nominal MPC
  GP-MPC has larger deviation than our method

## Slide 19
Simulations on Cart-Pole Stabilization with Inaccurate Model
Results:
Our method is computationally more efficient than GP-MPC

## Slide 20
Simulations on Cart-Pole Stabilization with Inaccurate Model
Results:
Prediction error decreases as we collect more data

## Slide 21
Simulations on Trajectory Tracking with Unknown Aerodynamic Effect
Goal:
Track reference trajectories with a drone
Setup:
The system dynamics of the drone are corrupted with unknown drag effects

## Slide 22
Simulations on Trajectory Tracking with Unknown Aerodynamic Effect
Goal:
Track reference trajectories with a drone
Setup:
The system dynamics of the drone are corrupted with unknown drag effects
GP-MPC
Nominal MPC
Ours
Ours w/ INDI
Compared algorithms: (i) Nominal MPC, (ii) Gaussian Process MPC12, and (iii) Ours w/ INDI inner loop13
12 Torrente et al., RAL '21
13 Tal et al., TCST '20

## Slide 23
Our Algorithm Achieves Lowest Tracking Errors

## Slide 24
Sample Trajectory w/ Maximun Speed > 10m/s
Results:
Ours achieves lower tracking errors than GP-MPC

## Slide 25
Hardware on Trajectory Tracking with Unknown Aerodynamic Effect
Goal:
Track a circular trajectory with a drone
Setup:
The circular trajectory is 1m in diameter
The speed is 0.8 m/s
The drone suffers from drag, voltage drop, communication delay, and:
(i) ground effect
(ii) wind disturbances
(iii) ground effect + wind disturbances

## Slide 26
Hardware on Trajectory Tracking with Unknown Aerodynamic Effect
Goal:
Track a circular trajectory with a drone
Setup:
The circular trajectory is 1m in diameter
The speed is 0.8 m/s
The drone suffers from drag, voltage drop, communication delay, and (i) ground effect, (ii) wind disturbances, and (iii) ground effect + wind disturbances
Compared algorithms: (i) Nominal MPC and (ii) L1 adaptive MPC14
14 Wu et al., TCST '25

## Slide 27
Our Algorithm Achieves Lowest Tracking Errors
Results:
Nominal MPC crashes under ground effect & wind disturbances
Ours achieves lower tracking errors than L1-MPC, due to the benefit of predictive model of unknown disturbances

## Slide 28
Sample Trajectory with Ground Effect
Results:
Ours achieves lowest tracking errors
L1-MPC do not learn the disturbance model and has large error when the disturbances change abruptly
Nominal MPC has poor z-direction tracking error due to ground effect and battery’s voltage drop

## Slide 29
Sample Trajectory with Wind Disturbances
Results:
Ours achieves lowest tracking errors
Nominal MPC has poor z-direction tracking error due to ground effect and battery’s voltage drop

## Slide 30
Sample Trajectory with Ground Effect & Wind Disturbances
Results:
Ours achieves lowest tracking errors
Nominal MPC crashes under ground effect & wind disturbances

## Slide 31
Summary & Extension
Online control algorithm for partially unknown control-affine systems with:
simultaneous system identification and model predictive control
no-dynamic-regret performance guarantees
Extension:
Hybrid systems
Active learning
Uncertainty quantification